## Slide 1: Prediction of Freezing of gait for Parkinson disease
Master’s Defense Project

## Slide 2: Related Work till date... Papers on Detection of FoG
Detecting freezing of gait with a tri‑axial accelerometer in Parkinson’s disease patients
  Data Availability: Imposed by Spanish Agency for Drugs and Medical Devices (Spain), all relevant data are available upon request (Joan Cabestany, email:joan.cabestany@upc.edu and Daniel Rodríguez-Martin, email: daniel.rodriguez-martin@upc.edu). Data contains accelerometer readings obtained from waist worn device.
  Detection accuracy using SVM was above 90%.
Classification of walking patterns in Parkinson's disease patients based on inertial sensor data.
  Data:Not available publicly, no mention about providing if requested. (recorded gait kinematics with wireless inertial measurement system and designed an algorithm for automatic recognition and classification of walking patterns)
  Error rate:16%, using simple Neural Network with simple signal processing and rule based classification.
  Detecting Freezing-of-Gait During Unscripted and Unconstrained Activity.
    Data derived from the outputs of three triaxial accelerometer (ACC) sensors and one surface electromyographic (EMG) sensor worn by the PD patient.
    Used DNN(Dynamic Neural Networks) obtained accuracy of 97% with sensitivity detection about 82%.

## Slide 3: Related Work till date... Papers on Detection of FoG
Deep learning for freezing of gait detection in Parkinson’s disease patients in their homes using a waist-worn inertial measurement unit
  Data collected using inertial measurement placed on their waist.
  Tree bagging, Adaboost, LogitBoost, RUSBoost, RobustBoost, SVM Accuracy about 90%
Feature Learning for Detection and Prediction of Freezing of Gait in Parkinson’s Disease
  Dataset available: www.wearable.ethz.ch/resources/Dataset
  Unsupervised Feature Learning using PCA
Freezing of Gait Detection in Parkinson's Disease: A Subject-Independent Detector Using Anomaly Scores
  Dataset available: www.wearable.ethz.ch/resources/Dataset
  anomaly detection techniques to detect FoG events

## Slide 4: Related Work till date... Papers on Detection of FoG
Real-Time Patient Adaptivity for Freezing of Gait Classification Through Semi-Supervised Neural Networks
  collected a dataset consisting of 25 patients wearing IMUs on their ankles.
  Proposed model to provide patient adaptivity in real-time through semi-supervised neural networks which exploit the stream of unlabeled data generated during usage. The overall patient-adaptive classifier resulted in 95.90% and 93.05% in sensitivity and specificity, respectively.
A smartphone based system for freezing of gait monitoring for Parkinson's disease patients
  Data was collected from PD patients from the system contained a wearable accelerometer mounted on the lower back of the patient and a smartphone as the computing unit.
  Model, Used was combination of FI(Freezing Index) based and RMS-based algorithm.
Modeling, Detecting, and Tracking Freezing of Gait in Parkinson Disease using Inertial Sensors
  Three-axis accelerometer sensor and three axis gyroscope sensors were combined and placed in the patient foot.
  Test framework to develop a two-stage detector for determining the zero-velocity and trembling events during gait, using this method 81.03% accuracy obtained in detecting FOG events.

## Slide 5: Related Work till date... Papers on Detection of FoG
  An anomaly detection technique in wearable wireless monitoring systems for studies of gait freezing in Parkinson's disease
    Using acceleration data and spectral analysis obtained from wearable assistant system.
    Proposed an online/real-time detection technique using anomaly detection and finally obtained an accuracy of about 87% on sensitivity and 94% on specificity.
Smart Gait-Aid Glasses for Parkinson's Disease Patients
  collected data under the supervision of a clinician by conducting 5 Timed-Up-and-Go (TUG) with gait-aid glasses and ankle-worn sensors
  System continuously monitors the gait and so on of a PD patient to detect FOG, and upon detection of FOG it projects visual patterns on the glasses as if the patterns were actually on the floor.
Detection of gait initiation Failure in Parkinson's disease based on wavelet transform and Support Vector Machine
  EEG data was obtained from five Parkinson's disease patients offers potential to study the behavior of GIF(Gait Initiation Failure).
  Novel methodology where wavelet transform was used for feature extraction and Support Vector Machine for classifying GIF events in five patients with PD and FOG.

## Slide 6: Related Work till date... Papers on Prediction of FoG
Utilizing Neural Networks to Predict Freezing of Gait in Parkinson’s Patients
  UCI Repository
  Layered Recurent Network with Accuracy of precision was 89% and recall was about 42%.
Prediction of Freezing of Gait in Parkinson's From Physiological Wearables: An Exploratory Study
  Dataset consist of electrocardiography and skin conductance data.
  Analysing data using one-way analysis of variance (ANOVA), and 2) mutual information (MI) values for each feature extracted
Prediction of freezing of gait using analysis of brain effective connectivity
  Dataset: The EEG data used in our study were collected from 10 patients (age with idiopathic Parkinson's disease and significant FOG as measured during a structured series of video-recorded timed up-and-go tasks
  For classification, MLP-NN was used due to its good results in classification of EEG signals [16]. A three layer Back Propagation Neural Networks with 4 to 5 hidden nodes was built

## Slide 7: Related Work till date... Papers on Prediction of FoG
Analysis and Prediction of the Freezing of Gait Using EEG Brain Dynamics
  This Paper Investigated the univariate and multivariate Electroencephalography (EEG) features determined by both Fourier and wavelet analysis in the confirmation and prediction of FOG
  This papers talks that EEG features are much better than accelerometer sensor detection process. This process helps in predicting FOG with accuracy of about 80%.
Prediction of Freezing of Gait in Parkinson's From Physiological Wearables: An Exploratory Study
  Analyzed electrocardiography (ECG) and skin-conductance (SC) data from 11 subjects who experience FoG in daily life, and found statistically significant changes in ECG and SC data
  Developed Anomaly based algorithm for predicting FOG from relevant SC features, prediction accuracy was about 71.3% with 4.2s before freeze episode happened.
Prediction of freezing of gait using analysis of brain effective connectivity
  Electroencephalography(EEG) data were acquired using a 4 channel wireless EEG system with gold cup electrodes.
  Multilayer Perceptron Neural Network used, with sensitivity, specificity and accuracy obtained in subject dependent analysis were 82%, 77%, and 78%.

## Slide 8: LSTM Results: Predicting with different time frames with batch size 1000 & vector size 50
Predicting
Predicting 1 second ahead
Accuracy: 87.54%
Predicting
Predicting 3 seconds ahead.
Predicting
Predicting 5 seconds ahead
Accuracy: 79.47%
Accuracy: 85.54%

## Slide 9: RNN Results: Predicting with different time frames with batch size 1000 & vector size 50
Predicting
Predicting 1 second ahead
Accuracy: 67.61%
Predicting
Predicting 3 seconds ahead.
Predicting
Predicting 5 seconds ahead
Accuracy: 61.34%
Accuracy: 65.9%

## Slide 10: Results: Training to predict for different time frame cycles Trained and tested on different users.
Batch size of 30, Predicting 1 Second ahead
1
Accuracy on the test set was 69.12%
Batch size of 30, Predicting 2.5 Seconds ahead
2
Batch size of 30, Predicting 5 Seconds ahead
3
Accuracy on the test set was 88.132%
Accuracy on the test set was 81.125%

## Slide 11: Results: Training to predict for different time frame cycles Trained and Tested on different users.
Batch size of 50, Predicting 1 Second ahead
1
Accuracy on the test set was 70.25%
Batch size of 50, Predicting 2.5 Seconds ahead
2
Batch size of 50, Predicting 5 Seconds ahead
3
Accuracy on the test set was 78.3524%
Accuracy on the test set was 81.5768%